## Slide 1
Objective:
To understand IPv6 implementation in the Intranet and Internet

## Slide 2
IPv6 Addressing Basics:
It is 128 bit long
0000000000000000:0000000000000000:0000000000000000:00000000000000000:0000000000000000:0000000000000000:0000000000000000:0000000000000000
Divide it into 8 groups of 16 bit each, with each group separated by a colon
They are converted to hexadecimal instead of the decimal conversion in IPv4.

## Slide 3
E.g.:
1100100000000001:000100011111111:
C 8 0 1 : 1 1 F F :
1111111011010100:000000000000
F E D 4 : 0 0 0
1000:0000000000000000:000000000000
8 0 0
0000:00000000000000000:00000000
0 0 0
00000001
0 1

## Slide 4
Cont.
So our IPv6 address will be:
C801:11FF:FED4:8::1

## Slide 5
With this basic let us now see what are the kind of IPv6 address we can have:
FE80: Link Local IPv6 address
2XXX: Global unicast IPv6 address
3XXX: Global unicast IPv6 address
FFXX: Multicast IPv6 address
**Anycast IPv6 address

## Slide 6
Link Local Address:
It start from FE80:: (network Address)
Rest is calculated by the system using the MAC address.
E.g.:
System MAC: CA01.11D4.0008
Link Local Address will be: FE80::C801:11FF:FEd4:8
Let us see how it is calculated by the system:
Step1: Convert the MAC Address to Binary
Binary of CA01.11D4.0008 will be
1100101000000001.0001000111010100.0000000000001000
Step2: Flip the 7th bit and then insert FFFE in the middle for the new EUI-64 Host ID
Here the 7th bit is 1 which will be flipped to 0 and so the first 4 hexadecimal digits will now be
1100100000000001 --------------------------- C801

## Slide 7
Cont.
And after inserting FFFE right in the middle of the newly calculated MAC address we get
C801.11FFFED4. 0008 which is
C801.11FF.FED4.8 (64 bit Host ID)
Thus the link local Address is:
FE80::C801:11FF:FED4:8
We can hard code the MAC address so as to get a link local address of our choice
Even the link local address can be hard coded without changing the MAC address

## Slide 8
Global IPv6 Address:
Global IPv6 address are currently assigned in the range 2XXX and 3XXXX
They can also be hard coded in the system.

## Slide 9
Multicast IPv6 Address:
Every host joins a special multicast group based on the last 24 bits of its host ID
*The solicited node multicast group is:
FF02::1:FFxx:xxxx
Where xx:xxxx = last 24 bits of host ID
Also every device joins a multicast group of FF02::1 by default

## Slide 10
Anycast Address:
An IP address that you can use on 2 or more device
The keyword “Anycast” disables Duplicate Address Detection (DAD)
E.g.:
Consider 2435::9/64 is the IP address assigned in two different networks as DNS address and a third router is trying to reach it from yet another network.
The routing protocols will sort out which 2345::/64 network is the “closest”.

## Slide 11
THANK YOU