## Slide 1
Objective
Understand Network
Understand IP Addressing (IPv4 and IPv6)
Understand Subnetting
Examples
IP addressing and Vlan’s in TIFR
TIFR network diagram
IP allocation in TIFR
Current IP database maintenance in TIFR
What is expected out of this project?

## Slide 2: Understand Network
A simple computer network for file sharing

## Slide 3
10/100 Ethernet Switch

## Slide 4: IPv4 Addressing
It is 32 bit long and divided into 4 octets. Each octet is 8 bit or 1 byte long. Octets are separated by dots. Total IPv4 addresses available are around 4.3 Billion.
An IPv4 address is represented in decimal form.

## Slide 5: IPv4 Addressing (Cont.)
Network Classes
Classes of network were created based on network size. Following are the classes of network:
8bits 8bits 8bits 8bits
Class A Network Host Host Host
Class B Network Network Host Host
Class C Network Network Network Host
Class D Multicast
Class E Research

## Slide 6: IPv4 Addressing (Cont.)
Binary to decimal conversion: (Cont.)
1 1 1 0 1 1 0
1x2^7+1x2^6+1x2^5+1x2^4+0x2^3+1x2^2+1x2^1+0x2^0
=128+64+32+16+0+4+2+0
=246

## Slide 7: IPv4 Addressing (Cont.)
Network Address Range: Class A
The first bit of the first byte in a Class A network
address must always be off or 0
0xxxxxxx
If we turn the other 7 bits all off and then all on, we
get the Class A range of Network addresses
00000000 = 0
01111111 = 127

## Slide 8: IPv4 Addressing (Cont.)
Network Address Range: Class B
In Class B network the first bit of the first
byte must always be turned on and the
second bit must always be turned off.
If you turn the other 6 bits all off and then all on,
you will find the range for a Class B network:
10000000 = 128
10111111 = 191

## Slide 9: IPv4 Addressing (Cont.)
Network Address Range: Class C
For Class C networks the first 2 bits of the
first byte as always turned on but the third
bit can never be on. Here is the range of
Class C network:
11000000 = 192
11011111 = 223

## Slide 10: IPv4 Addressing (Cont.)
Network Address Range: Class D
224-239
Network Address Range: Class E
240-255

## Slide 11: IPv4 Addressing (Cont.)
Private IP addresses:
Class Reserved Address Space
Class A 10.0.0.0 to 10.255.255.255
Class B 172.16.0.0 to 172.31.255.255
Class C 192.168.0.0 to 192.168.255.255

## Slide 12: IPv4 Subnetting
What is the need for Subnetting?

## Slide 13: IPv4 Subnetting (cont.)
Subnetting IP Addresses:
When subnetting all you need to do is answer five simple questions:
How many subnets does the chosen subnet mask produce?
how many valid hosts per subnet are available?
What are the valid subnets?
What’s the broadcast address of each subnet?
What are the valid hosts in each subnet?

## Slide 14: IPv4 Subnetting (cont.)
Answers:
How many subnets?
2^x= number of subnets. X is the number of masked bits or the 1’s
Example: 11000000 = 2^2 = 4 subnets
How many hosts per subnet?
2^y = number of hosts per subnet. Here y is the number of unmasked bits or 0’s.
Example: 11000000 = 2^6 = 64 hosts.

## Slide 15: IPv4 Subnetting (cont.)
What are the valid subnets?
256-subnet mask = block size or increment number.
Example: 256-192 = 64 So the valid subnets are 0, 64, 128, 192

## Slide 16: IPv4 Subnetting (cont.)
What’s the broadcast address for each subnet?
The last IP of each subnet is the broadcast address
What are the valid hosts in each subnet?
2^y-2 = number of hosts per subnet. Here y is the number of unmasked bits or 0’s.
Example: 11000000 = 2^6-2 = 64-2 = 62 usable hosts.

## Slide 17: IPv4 Subnetting (cont.)
Practice:
- Class C:
-> Subnet Mask = 255.255.255.128 (/25)
IP = 192.168.10.0
Answer: Binary of 128 is 10000000
Hence,
How many subnets?
2^x = 2^1 = 2 where x is the number of 1’s
How many usable hosts per subnet?
2^y-2 = 2^7-2 = 128-2 = 126 where y is the number of 0’s
What are the valid subnets?
256-128 = 128 (Block size)

## Slide 18: IPv4 Subnetting (cont.)
So we get following details for the 192.168.10.0/25 subnet:
First subnet: 192.168.10.0 to 192.168.10.127
Subnet ID: 192.168.10.0
Network ID: 192.168.10.127
Usable Hosts range: 192.168.10.1 to 192.168.10.126 i.e 126 usable IP addresses
Second Subnet: 192.168.10.128 to 192.168.10.255
Subnet ID: 192.168.10.128
Network ID: 192.168.10.255
Usable Hosts: 192.168.10.129 to 192.168.10.254 i.e 126 usable IP addresses

## Slide 19: IPv4 Subnetting (cont.)
Practice: (Cont.)
-> Subnet Mask = 255.255.255.192 (/26)
IP Address range: 192.168.10.0
Answer: Binary of 192 is 11000000
Hence,
How many subnets?
2^x = 2^2 = 4 where x is the number of 1’s
How many usable hosts per subnet?
2^y-2 = 2^6-2 = 64-2 = 62 where y is the number of 0’s
What are the valid subnets?
256-192 = 64 (Block size)

## Slide 20: IPv4 Subnetting (cont.)
So we get following details for the 192.168.10.0/26 subnet:
First subnet: 192.168.10.0 to 192.168.10.63
Subnet ID: 192.168.10.0
Network ID: 192.168.10.63
Usable Hosts range: 192.168.10.1 to 192.168.10.62 i.e 62 usable IP addresses
Second Subnet: 192.168.10.64 to 192.168.10.127
Subnet ID: 192.168.10.64
Network ID: 192.168.10.127
Usable Hosts: 192.168.10.65 to 192.168.10.126 i.e 62 usable IP addresses

## Slide 21: IPv4 Subnetting (cont.)
Practice: (Cont.)
Third subnet: 192.168.10.128 to 192.168.10.191
Subnet ID: 192.168.10.128
Network ID: 192.168.10.191
Usable Hosts range: 192.168.10.129 to 192.168.10.190 i.e 62 usable IP addresses
Fourth Subnet: 192.168.10.192 to 192.168.10.254
Subnet ID: 192.168.10.192
Network ID: 192.168.10.254
Usable Hosts: 192.168.10.193 to 192.168.10.253 i.e 62 usable IP addresses
So by /25 we lose 4 IP addresses and by /26 we lose 8 IP addresses

## Slide 22: IPv4 Subnetting (cont.)
Practice: (Cont.)
Subnet Mask: 255.255.255.224 (/27)
IP address range: 192.168.10.0
Answer:
Subnet Mask: 255.255.255.240 (/28)
IP Address range: 192.168.10.0
Answer:
Subnet Mask: 255.255.255.248 (/29)
IP Address range: 192.168.10.0
Answer:

## Slide 23: IPv4 Subnetting (cont.)
Class B Address Subnetting
Practice:
-> Subnet Mask: 255.255.128.0 (/17)
IP address range: 158.144.0.0
Answer: Binary of 128 is 10000000
Hence,
How many subnets?
2^x = 2^1 = 2 (same as Class C) where x is the number of 1’s
How many usable hosts per subnet?
2^y-2 = 2^15-2 = 32766-2 = 32764 where y is the number of 0’s
What are the valid subnets?
256-128 = 128 (Block size)

## Slide 24: IPv4 Subnetting (cont.)
So we get following details for the 158.144.0.0/25 subnet:
First subnet: 158.144.0.0 to 158.144.127.255
Subnet ID: 158.144.0.0
Network ID: 158.144.127.255
Usable Hosts range: 158.144.0.1 to 158.144.127.254 i.e 32764 usable IP addresses
Second Subnet: 158.144.128.0 to 158.144.255.255
Subnet ID: 158.144.128.0
Network ID: 158.144.255.255
Usable Hosts: 158.144.128.1 to 158.144.255.254 i.e 32764 usable IP addresses

## Slide 25: IPv4 Subnetting (cont.)
Class B Address Subnetting
Practice:
-> Subnet Mask: 255.255.192.0 (/18)
IP address range: 158.144.0.0
Answer:
-> Subnet Mask: 255.255.224.0 (/19)
IP address range: 158.144.0.0
Answer:
-> Subnet Mask: 255.255.240.0 (/20)
IP address range: 158.144.0.0
Answer:
-> Subnet Mask: 255.255.248.0 (/21)
IP address range: 158.144.0.0
Answer:
-> Subnet Mask: 255.255.252.0 (/22)
IP address range: 158.144.0.0

## Slide 26
5. IP addressing and Vlan’s in TIFR
IPv4 block assigned to TIFR: 158.144.0.0/16
6. TIFR network diagram
7. IP allocation to users in TIFR
8. Current IP database maintenance in TIFR
9. What is expected out of this project?