## Slide 1: Design and Development of Software Tools
An experience from the TIFR-INO team
Deepak Samuel

## Slide 2: INO-ASET Series
Overview and status of INO and ICAL: N.K.Mondal
Mechanical structure of ICAL detector: Piyush Verma
Magnet design: Vivek Datar
Gas systems for the ICAL detector: Suresh Kalmani
DAQ system for the ICAL prototype: Suresha Upadhya
Generator, simulations and reconstruction: Gobinda Mujumder
Today’s Talk: Deepak Samuel
VLSI and ASIC designs: V.B.Chandratre
DAQ system for the ICAL detector: B.Satyanarayana
Web utilities and on-line tools: P.Nagaraj

## Slide 3
“Each one of us adds a little to our understanding of nature and from all the facts assembled arises a certain grandeur”
-Aristotle

## Slide 4: Overview
Introduction to INO
Role of Software in HEP
Software Design Philosophy in INO
Applications for INO

## Slide 5: Main Objectives of INO
Reconfirm Neutrino Oscillations
Sign of δ32
Dirac or
Majorana ?
Long Base-line
Neutrino Detector
Template for Future Experiments

## Slide 6: INO-ICAL
28,000 RPC’s
50 k ton Iron
1.3 Tesla Magnetic Field
3.6 Million Channels

## Slide 7: Prototype Stack at TIFR
12 Layers
1m x 1m RPC’s
32 Strips/Plane
No Iron Layers

## Slide 8: Role of Software in HEP
Experiment
Simulation
Data Acquisition
Analysis, Graphing
Hardware Control, Monitoring

## Slide 9: Software used in HEP
GEANT
Simulation Package
MATLAB
OPENSCIENTIST
ROOT
Data Analysis Framework
Data Analysis Framework
Graphical programming environment
LABVIEW
Numerical/Symbolic computing environment

## Slide 10: Design Philosophy
Latest Technologies
Portability of Codes across platforms
Simplicity of Coding/Debugging
Simplicity of Use
All complexities invisible to the user
Always Scope for Improvement
Comments/ Documentation

## Slide 11: Basic Elements of INO Software
Programming Language
C, C++, Java?
Graphing/Analysis
Integrated Plotting and Analysis
Data Structure
OS independent, universal
Graphical User Interface
Simplicity of Use
C++
ROOT
QT

## Slide 12: ROOT
Statistical and Graphing Package
Freely available in CERN’s website
C++
Widely used in HEP
C++ interpreter CINT
Well documented
User Support available

## Slide 13: Graphing
ROOT Canvases (TCanvas Class)
Graphing/Analysis easier if native data structures used (root files)
Easily available fitting menus, Analysis tools
supports histograms, 2D, 3D graphs.

## Slide 14: Data Structure
Usual scenario: Storage of large quantities of same type of Structures.
Event Number
Particle Type
E
Px
Py
Time
Reaction
Vertex
Pz
EVENT TREE

## Slide 15: ROOT’s TTree Class
Key to an integrated Graphing and Analysis framework
Offers good compression (up to factor 10)
Optimized data access:
Example compute E2-P2

## Slide 16: Optimized Data Access with TTree
Read Entire Event n
Extract E, Px, Py, Pz
Compute
Without TTrees
With TTrees
Read Branches E,Px,Py,Pz only, from Event n
Compute

## Slide 17: Plotting/Analysis with TTree
Just need the branch name
Histogram : Tree->Draw(“E”)
Graphs: Tree->Draw(E: (px2+py2+pz2))
Conditional Plotting:
Tree->Draw(“E”,”EventNumber>25”)

## Slide 18: Additional Features
Friends
For example- Comparison of results from two different algorithms
Storing a selection
Cuts

## Slide 19: Software Development Tool
Cross-platform application and UI framework
Intuitive C++ class library
Integrated Development Tools
Available for Linux, Windows & Mac
FREE!!!

## Slide 20: Graphical User Interface
Designed using Qt Designer

## Slide 21: Integrated Development Tool

## Slide 22: Integrating ROOT and QT – QTROOT Plugin
Need to embed ROOT canvas into our GUI
A complete plotting and analysis environment inside our applications
QtROOT developed by BNL
Still in its nascent stage
TIFR- one of first few groups to use it for a large scale experiment

## Slide 23: Data Analysis Framework for NUANCE

## Slide 24: A modern visualization interface for GEANT

## Slide 25: Track display for GEANT simulation*

## Slide 26: VME Based DAQ Software*

## Slide 27: Offline Data Analysis Tool**

## Slide 28: VME DAQ Software-Comparison

## Slide 29: Design of VME DAQ Software
Muon
Signal
Y Strip
X Strip

## Slide 30: Design of VME DAQ Software
Trigger
Event (Hit Info + Timing)
Noise Rate Monitor
Data

## Slide 31: Back-End: VME Module Access
Each Module Type (Scaler, TDC etc.,) represented by a C++ class
All VME Classes inherit another general class “vmefunctions”
Seamless integration of VME Read/Write functions into our application
class v830CAEN:public vmefunctions // SCALER V830 CAEN
{
public:
unsigned long CHENBL; //Channel Enable
unsigned long CTRLREG; // control reg
unsigned long STATREG;// status register
unsigned long GEOREG;// GEO register
unsigned long INTLVL;// interrupt level
unsigned long INTVEC;// interrupt vector
unsigned long RESET; //reset
unsigned long SOFTTRG;//software trigger
unsigned long TRGCNTR;//trigger counter
unsigned long FULL;// almost full level
unsigned long CONFROM;// configuration rom
unsigned long FIRMWARE;// firmware
v830CAEN(unsigned long base, int modindx, QString modtyp); // constructor
void Reset(); //reset module
void Initialize();
};
GUI Framework
Read/Write
TDC
Scaler
vmefunctions
VME Library
Modules
Control/RO
If(Square)
a=b
If(Triangle)
b=b/2
Area = (a*b)
Square
Rectangle
Customized Class
Common Method (Library)
Shapes
Triangle

## Slide 32: Back-End: Interrupt Sources
Interrupt Sources
Scaler
(Monitor)
Periodic
Least Priority
TDC
(Event)
Random
Highest Priority

## Slide 33: Back-End : Threads
Threads allow a single program to have concurrently executing parts.
Threads can be thought of as mini-programs within a program.
Each thread will execute independently and concurrently with its own sequence of instructions.
Threads require synchronization (IPC) for concurrent read/write access to memory.
One Bad Thread Can Kill the Entire Program.
Parallel and Distributed Programming Using C++ By Cameron Hughes, Tracey Hughes

## Slide 34: Back-End : Multithreading
Start
Interrupt
Service
Thread
Event Thread
Monitor Thread
Event Plot Thread
Time Critical Priority
Highest Priority
Least Priority

## Slide 35: Interrupt Service Thread
Wait on Interrupts
Read IRQ Vector
Read Scaler/ TDC, Event Data
Write Data to Shared Circular Buffer
IPC-Trigger
Event Thread
Monitor Thread

## Slide 36: Event/Monitor Thread
Wait on event (IPC)
Read data from circular buffer
Check if file is free
Write data to file
Pass Hit Data to Plotting Thread and Web Update

## Slide 37: Inter-Process Communication (IPC)-Event
IST
Event Thread
Thread Synchronization using “Event” (IPC object).
Event: A software trigger.
Threads wait (passive) on a Event.
A Thread can miss an Event !
Monitor
Thread
Event Plot
Thread

## Slide 38: Inter-Process Communication (IPC)-Mutex
Mutually Exclusive access to shared resources
Threads first check if a mutex is unlocked
If unlocked, locks the mutex
After accessing the resource the thread should unlock mutex
int a = 0
(FILE)
Thread A (Event Thread)
a=5
Thread B
a=6
Thread C
(User Plot)
Read a
Mutex Lock

## Slide 39: Front End- GUI-Layout
MAINWINDOW
MENU BAR (Miscellaneous Options)
TOOL BAR
(Often used)
TEXT OUTPUT AREA (Dock Widget)
(Error/Status Messages)
MONITOR TABLE (Dock Widget)
(STRIP RATE)
i) VME Modules Settings
ii) Plotting Canvas Area
Event
Timing
Others
Each accessible via Menu Bar also
Plotting Input Area (Dock Widget)

## Slide 40: The Graphical User Interface

## Slide 41: Offline Analysis Tool
Analysis using CERN’s ROOT framework
GUI based tool
Fit parameters of tracks
Layer Multiplicity
Custom plotting without entering ROOT terminal
Is being currently upgraded to have extra features like custom fitting and better algorithms

## Slide 42: Offline Analysis Tool - GUI

## Slide 43: Track Viewer- A GEANT Simulation Add-on
Nuance: Event Generation: Neutrino + Iron = A + B +C + …
GEANT: Propagation of A+B+C+ … in the detector
Reconstruction: From E,P of A+B+C + … Get E,P of Neutrino
Track Finding and Fitting algorithms

## Slide 44: Sample Simulation Tracks

## Slide 45: Fitting and Finding of Tracks
Reconstruction is a complex algorithm (Kalman Filter, Fitting Models etc.,) – [Prof. Gobinda Majumder]
GEANT : (x,y,z,t) coordinates of the hits of particles in the detector.
Hits
Clusters
Triplets
Find Track
Fit Tracks
Output of these algorithms are plain numbers
Debugging a messy job !

## Slide 46: Track Viewer Tool

## Slide 47: View Options

## Slide 48: View Options

## Slide 49: Track Viewer- Debugging

## Slide 50: Track Viewer-Summary
Exposed the hitherto hidden bugs in the Reconstruction Algorithm
A powerful tool to individually sort out issues at every part of the reconstruction
Integrated with NUANCE analysis framework
Soon to be converted into a complete analysis framework for INO

## Slide 51: Qt- How to ?
Design your window using Qt Designer
Write your code in Qt Creator
Connect Signals to Slots

## Slide 52: Signal Slot Mechanism
Each Widget (Push Button, Text Box etc.,) emits different signals (Clicked, Double Clicked, Text Entered etc.,)
A slot is a function to which a signal is connected.
Connecting Signals to Slots done by “connect function”
connect(pushbutton, SIGNAL(Clicked()), mainwindow, SLOT(Close()));

## Slide 53: Summary
TIFR – INO team has developed a wide range of customized software applications.
Gained an experience in developing advanced software applications
This experience is a strong base for developing many other applications not only for INO but for other groups as well.
Happy to share our experiences!

## Slide 54: Acknowledgements
Prof. N. K. Mondal
Prof. G. Majumder [Simulation Group]:
  Asmita, Sudeshna Dasgupta
Mr.B. Satyanarayana [Electronics, Detector R&D and DAQ team]:
  Upadhya, Nagesh.
  Mandar, Shinde, Shekhar, Manas, Sumanta, Salim.